## Slide 1: Status of Embedded Linux
Status of
Embedded Linux
December 2017
Tim Bird
Architecture Group Chair
LF Core Embedded Linux Project

## Slide 2: Nature of this talk…
Quick overview of lots of embedded topics
A springboard for further research
  If you see something interesting, you have a link or something to search for

## Slide 3: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 4: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 5: Kernel Versions
Linux v4.9 – 11 Dec 2016 – 70 days
Linux v4.10 – 19 Feb 2017 – 70 days
Linux v4.11 – 30 Apr 2017 – 70 days
Linux v4.12 – 2 Jul 2017 – 63 days
Linux v4.13 – 3 Sep 2017 – 63 days
Linux v4.14 – 12 Nov 2017 – 70 days
Linux v4.15-rc1
  4.15 – I predict: 21 Jan 2018 (70 days))

## Slide 6: Linux 4.9
Virtually mapped kernel stacks
  http://lwn.net/Articles/692953/
  Allows to detect stack overruns
  Cleans up kernel code, faster process creation
  Only on x86, for now
Greybus - https://lwn.net/Articles/715955/
Timed samples for eBPF
Modversions deprecated
  See https://lwn.net/Articles/707520/

## Slide 7: Linux 4.10
Perf sched timehist
Hybrid block polling
  Supports polling for block I/O, but with a short delay (estimated) before the polling starts
    Improves performance by queuing blocks as soon as device is ready (via polling)
    Uses less CPU than full polling
Support for ARM SoCs:
  Huawei, Allwinner, Marvel, Renesas
Posix timers are configurable
Initramfs compression method is selectable
New interface for system sleep state selection
  /sys/power/mem_sleep
UBIFS support for encryption

## Slide 8: Linux 4.11
New kernel refcount API
TinyDRM subsystem added
New statx() system call
  https://lwn.net/Articles/707602/
  2038-safe time values
  Mask of fields to obtain (for efficiency)
Sched.h refactoring
  Non-mainline code: watch out!

## Slide 9: Linux 4.12
BFQ and Kyber block I/O schedulers
Mini-tty prep work
  Not full mini-tty implementation yet
Proper support for USB type-C connectors
AnalyzeBoot tool
  Reads dmesg (and possibly ftrace log) and produces html graph of boot events
  Part of Intel pm-graph tools project
    https://github.com/01org/pm-graph
  See tools/power/pm-graph/analyze_boot.py

## Slide 10: Linux 4.13
TLS implementation in the kernel
  Should help with HTTPS performance
  See https://lwn.net/Articles/666509/
Next-interrupt prediction
F2FS support for disk quotas
Kselftest transitioning to TAP13 protocol

## Slide 11: Linux 4.14
New kernel stack unwinder (ORC) for x86_64
  Better unwinding via kernel-specific out-of-band structure (for every kernel PC address)
  See https://lwn.net/Articles/728339/
zstd compression for btrfs and squashfs
Better cpufreq coordination with SMP

## Slide 12: Linux 4.15 (expected)
Cramfs supports mapping persistent memory
  Can use for XIP
AMD display core system accepted
  130k driver!
Device tree compiler has support for overlays

## Slide 13: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 14: Bootup Time
Analyze_boot tool – new in in 4.12
Some good previous talks:
  ELCE 2017 - A Pragmatic Guide to Boot-Time Optimization by Chris Simmonds
  ELCE 2014 - 12 Lessons Learnt in Boot Time Reduction by Andrew Murray
  ELC 2015 - Fastboot Tools and Techniques by John Mehaffey
Android boot time ideas
  ELC 2017 – Improving the bootup speed of AOSP – Bernhard Rosenkranzer

## Slide 15: Device Tree
Device Tree validation
  Schema for binding language, validator for bindings and for device tree data
  New proposal for device tree validation by Pantellis and Grant Likely
Updated Device Tree specification
  Want to update material and make it more available
Overlays
  Device tree compiler has support for overlays

## Slide 16: File Systems
zstd compression for btrfs and squashfs (4.14)
  Faster and smaller compression/decompression
    https://clearlinux.org/blogs/linux-os-data-compression-options-comparing-behavior
  How to use it ( BTRFS):
    https://btrfs.wiki.kernel.org/index.php/Compression
  See https://www.phoronix.com/scan.php?page=news_item&px=Linux-4.14-Zstd-Pull
F2FS support for disk quotes (4.13, 4.15)
  Apparently used by Android
UBIFS support for encryption (4.10)

## Slide 17: Graphics
TinyDRM
  Provides graphic support for small simple displays (eg displays over i2C or SPI)
  Hope to replace framebuffer drivers over time
  See https://www.phoronix.com/scan.php?page=news_item&px=TinyDRM-Patches-Posted
Presentation
  ELC 2017 What Can Vulkan do for You? - by Jason Ekstrand

## Slide 18: GPU drivers
Nvidia, Vivante and Broadcom GPUs have open drivers
  Nouveau, Etnaviv, and VideoCore 4
Qualcomm Adreno
  Freedreno continues to be developed (June 2017)
    See https://www.xda-developers.com/open-source-adreno-project-freedreno-receives-new-update/
Imagination PowerVR – no public driver, although one was teased in 2015
  Apple dropping Imagination (April 2017)
ARM Mali – Some work (Lima project) on earlier chip versions
  Status update: https://lwn.net/Articles/716600/
  Some recent work:
    https://github.com/yuq/linux-lima
    https://notabug.org/cafe/chai

## Slide 19: Networking
Time Sensitive Networking
  ELCE 2017 Deterministic Networking for Real-Time Systems (Using TSN) – by Henrik Austad
  so_txtime option for high-resolution transmit time
  IEEE deterministic networking (DetNet) working group
    Lots of standards

## Slide 20: Power Management
Power-efficient workqueues
  More efficient work scheduling
    Results in about 15% better energy consumption
    See https://lwn.net/Articles/731052/
Better cpufreq coordination with SMP
  Allows non-local CPU to adjust frequency
    Good for when a non-local CPU schedules work on a CPU, and the work needs a frequency boost
  See https://lwn.net/Articles/732740/

## Slide 21: Real Time
Realtime Summit
  Realtime trouble, lessons learned
  Using Coccinelle to detect and fix nested execution context violations
  SCHED_DEADLINE: what's next?
  Future of tracing
  See https://lwn.net/Articles/738001/
Status of Prempt-RT patch
  Hotplug locking
  Timer wheel rework
  Big outstanding issue: dentry cache locking

## Slide 22: Real Time (cont.)
Presentations:
  ELCE 2017 Deterministic Networking for Real-Time Systems (Using TSN) – by Henrik Austad
  ELCE 2017 Measuring the Impacts of the Preempt-RT Patch – by Maxime Chevallier
  ELC 2017 Effectively Measure and Reduce Kernel Latencies for Real-time Constraints – by Jim Huang
  ELC 2017 Real-Time Linux on Embedded Multicore Processors – by Andres Ehmanns

## Slide 23: Security
Kernel hardening
  http://kernsec.org/wiki/index.php/Kernel_Self_Protection_Project
    Rare_write infrastructure
      Keep some code and data read-only most of the time
      https://lwn.net/Articles/724319/
  GCC plugins for kernel security
    Kernexec
      Prevent kernel from executing user-space code
    Structleak (mainlined in 4.11)
      Zero out kernel structures passed to user space, under some conditions
    See https://lwn.net/Articles/712161/
    Randstruct
      Randomize C structure layout
      See https://lwn.net/Articles/722293/

## Slide 24: Security Presentations
  ELC 2017 Securing Embedded Linux Systems with TPM 2.0 – by Philip Tricca
  ELCE 2017 Security Features for UBIFS – by Richard Weinberger

## Slide 25: System Size
Initramfs compression method is selectable
Nicolas Pitre work
  Configurable POSIX timers – in v4.10
    https://lwn.net/Articles/701095/
  Mini TTY
    Smaller implementation of TTY subsystem, for embedded
    Saves about 38K
    https://lwn.net/Articles/721074/
    People wanted refactoring of full-size TTY instead of new small implementation, but Nicolas said that wasn’t feasible

## Slide 26: System Size (cont.)
Shrinking the scheduler
  Drops features and eliminates realtime and deadline scheduler classes
  Saves about 20k
  https://lwn.net/Articles/725376/
  Lots of resistance to this
  Code complexity increase is not worth saving 20k (according to Ingo Molnar)
  Disagreement on whether Linux should support computers with sub-1MB memory

## Slide 27: Size Presentations
ELCE 2017 Embedded Linux Size Reduction Techniques – By Michael Opdenacker
  Great overview of reduction techniques and status
    Toybox and musl (smaller libc) are worth looking at
    Long list of things that can be worked on
Linaro Connect SFO 2017: Internet of Tiny Linux (IoTL): Episode IV – by Nicolas Pitre
  http://connect.linaro.org/resource/sfo17/sfo17-100/
LinuxCon North America: Running Linux on Tiny Peripherals – by Marcel Holtmann
  Got Linux to around 1MB for IOT sensor project

## Slide 28: Testing
Kselftest
Fuego
Kernelci.org
LAVA V2
Kernel regression tracking
Plumbers session on testing

## Slide 29: Kselftest
Unit test system inside kernel source tree
Recent work:
  -silent option, to reduce output clutter
  Support for O= option, to build outside source directory
  Lots more regression tests (preferred place for syscall compatibility/regression tests (over LTP)
  Converting to TAP (Test Anything Protocol) for test output ( started in 4.13)
See https://lwn.net/Articles/737893/

## Slide 30: Fuego
New Test Framework for collaborating on tests and test infrastructure for Linux
V1.1 features (April 2017)
  Upgrade to latest Jenkins
  Test script refactoring
  Fuego container directory layout change
  About 40 new tests
V1.2 plans (RC very soon (Sep 2017)
  Unified output format
    Convert all test results to JSON, in a format compatible with Kernel CI
  New pass criteria system
  Test dependency system
    Board dynamic variables

## Slide 31: Kernelci.org
Place to get free build/boot testing for your board
  Builds 126 trees continuously, then reports any errors
http://kernelci.org
Presentations:
  ELC and ELCE 2016 – by Kevin Hilman
  Linaro Connect:
    Kernelci and lava update - See https://lwn.net/Articles/716600/
The most successful public, distributed build and test system for Linux, in the world!

## Slide 32: LAVA
Linaro Automation and Validation Architecture
V2
  Job files now use Jinja2 templates
    Was previously hand-written JSON
  Jobs are run asynchronously, without polling,
  ZeroMQ is used for communications.
  ReactOBus is used to run jobs from messages.
  Requires more explicit board configuration

## Slide 33: Other efforts
Kernel regression tracking
  Thorsten Leemhuis reported at kernel summit issues and difficulties doing regression tracking
    Kernel developers don’t like Bugzilla
    Not enough people doing this work (no community effect)
    Errors on specific hardware are hard to reproduce
    Would be good to identify sub-systems with more regressions and target those for more testing
  See https://lwn.net/Articles/737666/ and https://lwn.net/Articles/738216/
Plumbers sessions on testing
  See https://lwn.net/Articles/734016/ and https://lwn.net/Articles/735034/

## Slide 34: Toolchains
LLVM 4.0.0 is released
  Some code size improvements from optimizations (GVNHoist)
  Experimental support for LLVM coroutines
  https://lwn.net/Articles/716979/
Presentations:
  ELC 2017 - GCC/Clang Optimizations for Embedded Linux – by Khem Raj
  Plumbers 2017 Building the kernel with Clang – by Nick Desaulniers
    https://lwn.net/Articles/734071/

## Slide 35: Tracing
More perf tools (both in 4.10):
  perf sched timehist
    Analysis of scheduling events
  perf c2c
    Cacheline contention analysis
Presentations:
  ELC 2017 Dynamic Tracing Tools on ARM/AArch64 Platform: Updates and Challenges - by Hiroyuki Ishii
    Great overview

## Slide 36: Miscellaneous
Printk issues
Year 2038 work
Linus issues with Kconfig
AGL making inroads
Android mainlining status
Linux in Supercomputers
FreeRTOS switched to MIT license

## Slide 37: Printk issues
Discussion on kernel summit mailing list
  Lots of issues with printk
    It’s not per-CPU, console lock held too long, it has complicated code paths, and lots more
  See thread start at:
    https://lists.linuxfoundation.org/pipermail/ksummit-discuss/2017-June/004358.html
Recent discussions about KERN_CONT
  KERN_CONT is unreliable for SMP kernels
  Latest kernelput ‘\n’ between lines that don’t have KERN_CONT
  Eventual removal of KERN_CONT
    Maybe use of seq_buf for outputting serialized date atomically
  https://lwn.net/Articles/732420/

## Slide 38: Year 2038 work
3 areas of work
  Converting all 32-bit timestamps to 64-bit in the kernel
    e.g. New statx() system call
    Many patches are in-progress (vfs layer, v4l, device-mapper, input subsystem)
  C libraries
    Lots of work in glibc to make everything backwards compatible
      Even programs built with 32-bit timestamps should work
  Distribution builds – fixing up individual packages
See https://lwn.net/Articles/717076/

## Slide 39: Linus issues with Kconfig
Discussion on kernel summit mailing list
  Kconfig is too hard for end users
  What can be done?
  Linus’ complaint:
    https://lists.linuxfoundation.org/pipermail/ksummit-discuss/2017-June/004504.html
Ideas:
  Config fragments
  Higher level options
  Better dependencies
    From distro feature to kernel config

## Slide 40: AGL status
First car in US with Entune (AGL-based infotainment OS) will be 2018 Toyota Camry
  Announced at Open Source Summit Japan by Toyota
Mazda and Toyota collaborating on Entune
  https://www.theregister.co.uk/2017/08/29/mazda_toyota_linux_entune_car_infotainment/

## Slide 41: Android mainline status
Lots of Android SoC support still out-of-tree
  Vendors are starting to mainline things, but it will take time (many years)
  Android kernels for shipping devices are likely to remain 2-years behind mainline
    LTS support expires at 2 years
    Greg will maintain some LTS kernels for 6 years, but stop if vendors don’t use it
  There is interest in improving LTP
    But mainline on Android devices would be better
  See https://lwn.net/Articles/738225/ for report by Greg Kroah-Hartman

## Slide 42: Linux in Supercomputers
Linux now runs 100% of the top 500 supercomputers
  As of November, 2017
  Was 99.6% (498 out of 500) in June 2017
  Most powerful machine, China’s “Sunway TaihuLight” uses 650,000 processors!
  See http://www.omgubuntu.co.uk/2017/11/linux-now-powers-100-worlds-top-500-supercomputers

## Slide 43: FreeRTOS license change
FreeRTOS switch to MIT license
  Richard Barry started working for Amazon last year
  Amazon released FreeRTOS version10 with MIT license
    Removed GPL v2 (with extra clauses)
    Added branding “fair use” clause to MIT
  Is a pretty big deal, IMHO
  See https://lwn.net/Articles/740372

## Slide 44: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 45: Projects and initiatives
Shared Embedded Distribution
LTSI
Fuego
eLinux wiki

## Slide 46: Shared Embedded Distribution
Goals
  Create an industry-supported distribution of embedded Linux
    Main goal is very long term support (15 years)
Status
  Working on building Debian with Yocto Project
  3 projects - meta-debian, isar and elbe wish to collaborate and combine their yocto recipes into a single layer.
Next steps
  Continued integration of Debian-based build and packaging systems

## Slide 47: Long Term Support Initiative
LTSI 4.9 is current LTSI kernel
  Work is in progress on next release 4.14
Most of industry is using LTS or LTSI
Using upstream-first policy for patches
Security fixes are very important
Presentation:
  ELCE 2017 Using Long Term Stable Kernel for the Embedded Products – by Tsugikazu Shibata

## Slide 48: Fuego - Linux Test Framework
Working on lots of issues
Presentation:
  Japan Jamboree 63: Fuego Status and Roadmap December 2017 – by Tim Bird

## Slide 49: eLinux wiki
http://elinux.org
  Web site dedicated to information for embedded Linux developers
    The wikipedia of embedded linux!
Hundreds of pages covering numerous topic areas: bootup time, realtime, security, power management, flash filesystem, toolchain, editors
Slides and Videos for 12 years of ELC!!
Please use and add to site

## Slide 50: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 51: Trade Associations
Linaro still doing lots of great work
  Lava v2 and kernelci
  Now promoting Zephyr
  Linaro Connect consistently has useful material
Linux Foundation
  Continuing to grow
    First event in China sold out in 2 weeks (1200 attendees)
  Over 100 conferences, 67 projects
    Not just Linux
  More than 500 members

## Slide 52: Conferences
ELC 2017
  See: http://elinux.org/ELC_2017_Presentations
Embedded Linux Conference Europe
  Lots of great sessions!
  See https://elinux.org/ELC_Europe_2017_Presentations
Embedded Linux Conference 2018
  March 12-14, Portland, Oregon, USA
Japan Jamborees
  Continuing
Open Source Summit Japan
  June 20-22, Tokyo, Japan
ELC Europe 2018
  October 22-24, Edinburgh, Scotland

## Slide 53: Legal Issues
SPDX adopted by Linux kernel
  Extensive review done of files without license identifiers
  Lots of files were tagged with SPDX license IDs
  See https://lwn.net/Articles/739183/
  and kernel commit: ead751507
    applied in 4.14-rc7!
    https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/commit/?id=ead751507de86d90fa250431e9990a8b881f713c
  Some complaints about process used for patch

## Slide 54: Outline
Kernel Versions
Technology Areas
CE Workgroup Projects
Other Stuff
Resources

## Slide 55: Resources
LWN.net
  http://lwn.net/
  If you are not subscribed, please do so
Kernel Newbies
  http://kernelnewbies.org/Linux_4.??
eLinux wiki - http://elinux.org/
  Especially http://elinux.org/Events for slides and videos
Celinux-dev mailing list

## Slide 56: Thanks!